## Slide 1: Lecture # 04M: Switch Debouncing
Course Teacher: Prof. Dr. Engr. Muhibul Haque Bhuyan
Professor, Department of EEE
American International University-Bangladesh (AIUB)
Dhaka, Bangladesh

## Slide 2: What is Debouncing?
When the state of a mechanical switch is changed from open to closed and vice versa, there is often a short period of time when the input voltage jumps between HIGH and LOW levels a couple of times before it settles. These transitions are called bouncing and getting rid of the effect of these transitions is called debouncing. To apply a manual switch signal into a digital circuit, we need to debounce the signal, so a single press doesn’t appear as multiple presses.
Alternatively, when a mechanical switch is flipped/pressed, the metal contacts inside may not open or close cleanly. In the microseconds before the switch achieves a good solid connection, the switch's contacts may "bounce" against each other, turning the switch on and off in rapid succession.
Example 1: If we connect the switch button to a pin with an external interrupt enabled, we will get several interrupts from pressing the button just once. This behavior causes multiple false button presses.
Example 2: Imagine using a button in a TV remote controller for the selection of a channel. If the button is not being debounced, one press can cause the remote to skip one or more channels.

## Slide 3: Why does Bouncing Happen?
Bouncing is a result of the physical property of mechanical switches.
Switch and relay contacts are usually made of metallic springs so when a switch is pressed, it is essential that two metal parts come together. But, this does not happen immediately, it bounces between in-contact (close the contact) and not-in-contact (open the contact) until it finally settles down.
Pull-down Resistor
Figure shows a simple push switch with a pull-down resistor and at its right, the output signal, Vout shows the signal bounces when the switch is pressed or depressed.

## Slide 4: Why does Bouncing Happen?
Figure shows a simple push switch with a pull-up resistor and at its right side, the trace shows the output signal, Vout, when the switch is pressed. As can be seen, pressing the switch does not provide a clean edge. If this signal is used as an input to a digital counter, for example, you will get multiple counts rather than the expected single count.
The same can also occur on the release of a switch.
The problem is that the contacts within the switch don't make contact cleanly, but slightly 'bounce'. The bounce is quite slow, so you can recreate the trace, and the problem quite easily.
Pull-up Resistor

## Slide 5: Why does Bouncing Happen?
The bouncing phenomenon is associated with the Single Pole Single Throw (SPST), Single Pole Double Throw (SPDT), and similar other types of toggle switches. The bouncing case data may be analyzed to see how long the switch bounce persists, how wide the individual bounce pulses are, and how many bounces are observed.
It is essential that the technique is not fooled by the occasional noise “glitch” or “spike” caused by other electrical, electronic, or electromagnetic signals, such as
    Crosstalk,
    EMI (electromagnetic interference)
    RFI (radio frequency interference)
    ESD (electrostatic discharge).

## Slide 6: How does Bouncing Happen?
In this diagram, resistor R1 is acting as a pull-up resistor.
  When the switch is open, R1 pulls the NO (Normally Open) contact to a positive (logic 1) value, usually +5 V.
  When the switch is closed, it shorts the NO contact to 0 V (logic 0).
We intend to get an output voltage of 5 V (logic 1) when the switch is not pressed, and 0 V (logic 0) when it is pressed.
But before the signal settles, it bounces between the two logic states several times.

## Slide 7: How to Avoid Bouncing?
The digital circuits and microcontrollers don’t like its input signals wandering around the undefined region between a “good” logic 0 and a “good” logic 1.
A standard buffer has single switching threshold, so a noisy signal or a signal with a bit of ripples on it, can result in multiple transitions at the output.
In 1934, a young graduate student named Otto Herbert Schmitt invented a circuit known as the Schmitt trigger (this invention was a result of Otto’s study into the propagation of neural impulses in the nerves of squids- a kind of sea fish) that has two thresholds. The output changes only when the input crosses the upper threshold (during upward transition) or the lower threshold (during downward transition) . This dual-threshold action is called hysteresis (the dependence of the state of a system on its history), which implies that the trigger possesses memory.

## Slide 8: How to Avoid Bouncing?
Single threshold
Dual thresholds
Hysteresis

## Slide 9: How to Avoid Bouncing?
In the RC network, we use a simple SPST switch debounce circuit, we would add a Schmitt trigger buffer between the RC network and the microcontroller as illustrated below.

## Slide 10: How to Avoid Bouncing?
We have shown a non-inverting Schmitt trigger buffer to keep things simple.
It is common to use an inverting Schmitt trigger buffer because inverting functions are faster than their non-inverting counterparts.

## Slide 11: Types of Debouncing
We can remedy this problem by debouncing the switch. There are many ways to do this. There are two general ways of getting rid of the bounces:
  Hardware debouncing: adding circuitry that gets rid of the unwanted transitions.
  Software debouncing: adding code/program that causes the application to ignore the bounces.
Besides, we can debounce the signals using the following techniques as well
  Digital Switch Debouncing: achieved in the same way as the software approaches
  Switch Debouncer using VHDL: The VHDL entity description is used.

## Slide 12: Hardware Debouncing
There are various implementations of circuits that can be used for eliminating the effect of switch debouncing right at the hardware level.
One of the most popular solutions using hardware is to employ a resistor/capacitor network with a time constant (t) longer than the time it takes the bouncing contacts to stop, i.e., t > tbounce.
Often it is also followed by a Schmitt trigger to get rid of the capacitor voltage values midway between HIGH and LOW logic.
If we wish to preserve program execution cycles, the best way is to use the hardware debouncing approach.
In hardware debouncing, we may use a flip-flop to ‘latch’ the signal, using a capacitor to absorb the bouncing periods.

## Slide 13: Hardware Debouncing Circuit
The following circuit is a simple hardware debouncing circuit with a switch for digital logic. When the switch is closed, the voltage is pulled down LOW through the switch, and when the switch is open, the output voltage is pulled up HIGH through the resistors R1 and R2. The resistor R2 prevents a short circuit when the switch is closed.
The capacitor absorbs the bounces when the switch changes states. Keep in mind that this circuit will cause a short delay in switching because the capacitor takes time to charge and discharge through the resistors.
The delay can be minimized by varying the values of the capacitor and resistor, but if the resistor is too small, it may not be sufficient to absorb the bounces.

## Slide 14: Hardware Debouncing Circuit
It is to be noted that the capacitor exhibits a curve when charging, and parts of this curve fall in the region where the logic circuit is undecided whether to treat it as a HIGH or LOW signals. To fix this problem, a Schmitt trigger is added to the output of the RC network.
Without Schmitt trigger RC network output
With Schmitt trigger digital output
Remember that the 7414 Schmitt trigger will invert the signal.
RC network output

## Slide 15: Hardware Debouncing
Circuit Design using the IC 7414 is a Schmitt trigger (inverting type buffer) with the input hysteresis.
A CMOS device like the 74AHCT14 dribbles about a mA from the inputs.
Resistances R1 and R2 control the capacitor’s charging-discharging time and thus set the debounce period for the switch open state.
The equation for charging is:
is the voltage towards which the capacitor will reach after the capacitor is completely charged. This is the supply voltage, in this case.

## Slide 16: Hardware Debouncing Circuit Design
The equation for discharging a capacitor is given by
Debouncing circuit design using the IC 7414 Schmitt trigger (inverting type buffer)
is the voltage from where the capacitor starts to discharge after the capacitor is completely charged.

## Slide 17: Hardware Debouncing Circuit Operation
The circuit’s operation can be explained by looking at the equivalent circuits formed in the two switching states, e.g., open and closed.
Now, CLOSE the switch:
The capacitor will discharge via R2 as per equation.
In time, C1 will discharge and Vb will reach 0 V.
Therefore, the output of the inverting Schmitt trigger will be a logic 1.
Starting with the switch OPEN:
The capacitor C1 will charge via R1 and D1 as per equation .
In time, C1 will charge and Vb will reach within 0. 7 V of Vcc.
Therefore, the output of the inverting Schmitt trigger will be a logic 0.

## Slide 18: Hardware Debouncing Circuit Design
What happens when the bounce occurs?
If bounce occurs and there are short periods of switch closure or opening, the capacitor will stop the voltage at Vb from immediately reaching Vcc or GND. Although bouncing causes slight charging and discharging of the capacitor, the hysteresis of the Schmitt trigger input stops the output from switching.
Why is a diode used?
The resistor R2 is required as a discharge path for the capacitor. Without it, C1 will be shorted when the switch is closed. Without the diode, D1, both R1 and R2 would form the capacitor’s charging path when the switch is open. The combination of R1 and R2 increases the capacitor’s charging time and thus slows down the circuit. With a diode, when the switch is closed, R1 limits the current flow, and the diode bypasses R2 as it is forward biased.

## Slide 19: Hardware Debouncing Circuit Design
The goal of the debouncing circuit design is to select R-C values that ensure the capacitor’s voltage stays above the threshold voltage, Vth around which the signal switches till the switch stops bouncing.
Most of the switches exhibit bounce times well under 10 ms, making the use of this value a conservative choice.
To calculate the R-C values considering this bounce time, we rearrange the capacitor’s charging-discharging formula as follows to solve for R (the cost and size of capacitors vary widely, so it is the best option to select a value for C arbitrarily and then compute R)

## Slide 20: Hardware Debouncing Circuit Design
Numerical Example:
The 74AHCT14 version has a worst-case Vth for a signal going low of 0.9 V, the higher threshold voltage, Vth,L.
Let us try with a 0.1 μF capacitor, since this is small, cheap, and will solve for the conditions in which the switch is closed.
We start our computation using the capacitor discharge formula. Since the capacitor discharges through R2, from this equation, we can get its value. We consider the power supply as 5 V (i.e., Vfinal = 5 V at the start of discharging).
Since a resistor with this value is not available, so we use 120 kΩ.
Considering bounce times as 20 ms

## Slide 21: Hardware Debouncing Circuit Design
Numerical Example (continuing):
But the analysis ignores the gate’s input leakage current when the signal is LOW at its input. A CMOS device like 74AHCT14 dribbles about 1 μA from the inputs.
As such, a 120 kΩ resistor may bias the input to 0.12 V (since as per Ohm’s Law, V), uncomfortably close to the gate’s best-case switching point of 0.4 V.
Therefore, the capacitor’s capacitance is increased to 1 μF from 0.1 μF and hence the resistor value decreases 10 times. So, we can use 12 kΩ for R2. A resistance of 12 kΩ is commercially available in the market.

## Slide 22: Hardware Debouncing
Numerical Example (continuing):
R1 + R2 controls the capacitor’s charging time and so sets the debounce period for the condition when the switch opens. The equation for charging is:
Solving for R:
Vfinal is the final charged value of the 5 V power supply. Vth,H is the worst-case transition point for a high-going signal, which for our 74AHCT14 is 1.7 V. So, (if no diode is used R2 won’t be shorted during charging).
Since, we have calculated R2 = 12 kΩ, hence, R1 = 48 – 12 = 36 kΩ.  Available

## Slide 23: Hardware Debouncing
Numerical Example (continuing):
The diode is an optional part. If we use a diode across R2 then it removes R2 from the charging circuit. All the charging current flows through the R1.
Equations will be the same except that we must take the voltage drop across the diode into account. Change Vfinal to 4.3 V (5 minus the 0.7 V of the diode’s forward voltage drop, VD) and solve for R1 and R2.
New computations are as follows
Considering bounce times as 20 ms and capacitance value as 1 mF

## Slide 24: Hardware Debouncing
Numerical Example (continuing):
Be wary of the components’ tolerances!
Standard resistors are usually ±5% (based on silver band as the 4th band on the resistor) to ±10% (based on gold band as the 4th band on the resistor), and the capacitors are ±20% (for electrolytic) to ±30% (for small ceramic capacitors) are error-prone from their nominal rating.
For example, if a resistor has nominal resistance value of 180 kW, and its 4th color band is silver color then the resistance value may vary between (180kW ± 5% of 180kW) i.e., from (180kW - 5% of 180kW) to (180kW + 5% of 180kW) or from (180 kW - 9kW) to (180 kW + 9kW) or from 171kW to 189kW.

## Slide 25: Hardware Debouncing (Summary)
After elapsing the de-bounce time, at t = tb, the capacitor voltage becomes equal to the higher threshold voltage when it is charging. That is, at t = tb, = higher threshold while the capacitor is charging.
Taking natural logarithm (ln) on both sides
;
During charging (Eq. 1), use if there is no diode in the circuit, and if there is a diode, use . If a diode is there, then you must use in both charging and discharging equations.
t = tb

## Slide 26: Hardware Debouncing (Summary)
After elapsing the de-bounce time, at t = tb, the capacitor voltage becomes equal to the lower threshold voltage when it is discharging. That is, at t = tb, = lower threshold while the capacitor is discharging.
Taking natural logarithm (ln) on both sides
;
During discharging (Eq. 2), use if there is a diode or no diode at all in the circuit. If a diode is there, then you must use in both charging and discharging equations.
t = tb

## Slide 27: Example 2 on Debouncing
A TV remote controller is to be designed with the channel selection buttons to be debounced. It was observed that the switches exhibit bounce times well under 20 ms. Design a circuit using the 74HC14 Schmitt trigger IC along with the resistance and capacitance. The worst-case Vth of this IC for a signal going low is 2.5 V, and that of when going high is 0.8 V. Also, consider that the CMOS device leakage current is 10 mA and the gate’s best-case switching point is of the order of 0.4 V. Compute the hysteresis voltage.
Answer:
While falling the signal, we choose a value of capacitance, C = 1 mF and use
After rearranging the equation, we get , and then putting the values, we find
For TTL IC family, we usually choose supply voltage, VCC = 5 V.

## Slide 28: Example 2 on Debouncing
If we choose this value, therefore, during discharging, due to the leakage current of 10 mA, a voltage drops of 1 V would occur, and it is not comfortably well below the gate’s best-case switching point of 0.4 V. Therefore, we can increase this capacitor’s capacitance to 10 μF so that the resistance of discharging path becomes and as such the voltage drop becomes .
During the rising the signal, we choose this capacitance value of C = 10 mF and use capacitor’s charging equation,
After rearranging the equation, we get , and then putting the values, we find

## Slide 29: Example 2 on Debouncing
Since, already we have calculated R2 = 1.1 kΩ, hence, R1 = 2.89 – 1.1 = 1.79 kΩ . These values are available; therefore, we will use 1.1 kΩ for R2 and 1.8 kΩ for R1. Therefore, the final designed circuit is given as follows
The hysteresis voltage is given by

## Slide 30: Example 3 on Debouncing
A TV remote controller is to be designed with the channel selection buttons to be debounced. It was observed that the switches exhibit bounce times well under 10 ms. A Si diode is used across the second resistor to make the duty cycle 50%. Design a circuit using the 74HC14 Schmitt trigger IC along with the resistance and capacitance. The worst-case Vth of 74HC14 for a signal going low is 2.3 V, and that of when going high is 0.95 V. Consider that the CMOS device leakage current is 5 A and the gate’s best-case switching point is of the order of 0.5 V. Compute the hysteresis voltage.
Answer:
While falling the signal, we choose a value of capacitance, C = 1 mF and use
After rearranging the equation, we get , and then putting the values, we find-
For TTL IC family, we usually choose supply voltage, VCC = 5 V.
Assuming the Si diode’s forward voltage drop, VD = 0.7 V.

## Slide 31: Example 3 on Debouncing
If we choose this value, therefore, during discharging, due to leakage current of 5 mA, a voltage drops of 034 V would occur, and it is comfortably well below the gate’s best-case switching point of 0.5 V. Therefore, we use this capacitor’s capacitance of 1 μF so that the resistance of the discharging path remains at and as such the voltage drop becomes .
Again, during rising the signal, we choose this capacitance value of C = 1 mF and use this in capacitor’s charging equation,
After rearranging the equation, we get , and then putting the values, we find
Neglecting a very small diode’s forward resistance.
Assuming the Si diode’s forward voltage drop, VD = 0.7 V.

## Slide 32: Example 3 on Debouncing
So, our calculated values for the designed circuit are R1 = 18 kΩ, R2 = 6.8 kΩ, and C = 1 mF. Therefore, the final designed circuit is given as follows
The hysteresis voltage is given by-

## Slide 33: Example 4 on Debouncing
A TV remote controller is designed with channel selection buttons to be debounced. It was observed that the switches exhibit bounce times well under 15 ms, and the duty cycle is 50%. Design a circuit using the 74HC14 Schmitt trigger IC along with resistance and capacitance. The worst-case Vth of this IC for a signal going low is 2.1 V, and that of when going high is 0.8 V. Also, consider that the CMOS device leakage current is 2 mA and the gate’s best-case switching point is of the order of 0.4 V. Compute the hysteresis voltage.
Answer:
While falling the signal, we choose a value of capacitance, C = 1 mF, and use After rearranging the equation, we get , and then putting the values, we find
For TTL IC family, we usually choose supply voltage, VCC = 5 V.

## Slide 34: Example 4 on Debouncing
If we choose this value, therefore, during discharging, due to the leakage current of 2 mA, a voltage drop of V would occur, and it is comfortably far away from the gate’s best-case switching point of 0.4 V. Therefore, we can choose this capacitor’s capacitance value of 1 μF so that the resistance of the discharging path is 8.2.
Again, during the rising of the signal, we choose this capacitance value, that is, C = 1 mF and use the capacitor’s charging equation, After rearranging the equation, we get , and then putting the values, we find

## Slide 35: Example 4 on Debouncing
Since, already we have calculated R2 = 8.2 kΩ, hence, R1 = 27.54 – 8.2 = 19.34 kΩ . Therefore, the final designed circuit is given as follows
The hysteresis voltage is given by
V

## Slide 36: Software Debouncing
Debouncing in hardware may give rise to additional cost, and it is more difficult to determine a good debouncing for all the push button switches that will be used. So, it may be preferable to debounce the switch in software.
Debouncing a switch in software is very simple. The basic idea is to sample the switch signal at a regular interval and filter out any glitches. There are a couple of approaches to achieving this. These approaches assume a switch circuit like that shown in the explanation of switch bounce- a simple push switch with a pull-up resistor.
While numerous algorithms exist to perform the debouncing function, we are going to limit ourselves to implementing two during the lab. Both approaches use a timer.

## Slide 37: Software Debouncing
Approach 1
The first approach uses a counter to time how long the switch signal has been low. If the signal has been low continuously for a set amount of time, then it is considered pressed and stable.
    1 Setup a counter variable, initialized to zero.
    2 Setup a regular sampling event, perhaps using a timer. Use a period of about 1 ms.
    3 On a sample event:
    4 if the switch signal is HIGH then
    5 RESET the counter variable to ZERO
    6 SET internal switch state to released
    7 else
    8 Increment the counter variable to a maximum of 10
    9 end if
    10 if counter=10 then
    11 SET internal switch state to pressed
    12 end if

## Slide 38: Software Debouncing
Approach 2
The second approach is like the first but uses a shift register instead of a counter. The algorithm assumes an unsigned 8-bit register value, such as that found in 8-bit microcontrollers.
    1 Set up a variable to act as a shift register and initialize it to 0xFF.
    2 Set up a regular sampling event, perhaps using a timer. Use a period of about 1 ms.
    3 On a sample event:
    4 SHIFT the variable towards the most significant bit
    5 SET the least significant bit to the current switch value
    6 if shift register value = 0 then
    7 SET internal switch state to pressed
    8 else
    9 SET internal switch state to released
    10 end if

## Slide 39: Software Debouncing
There are two more approaches to software debouncing.
In the first technique, wait for a switch closure, then test the switch again after a short delay (15 ms or so). If it is still closed, detect that the switch has changed state.
In the second technique, check the switch state periodically to see if it has changed its state.
When working with microcontrollers, we can deal with switch bounce in a different way that may save both hardware, space, and money. Some programmers do not care much about bouncing switches and just add a 50 ms delay after the first bounce. This forces the microcontroller to wait 50 ms for the bouncing to stop, and then continue with the program. This is not a good practice, as it keeps the microcontroller waiting.
Another way is to use an interrupt for handling the switch bounce. Be aware that the interrupt might be fired on both the rising and falling edge, and some microcontrollers might stack up one waiting interrupt.

## Slide 40: Software Debouncing
The following is a simple software debounce code for Arduino written in IDE
int inPin = 7; // the pin number of the input pin
int outPin = 13; // the pin number of the output pin
int counter = 0; // how many times we have seen new value
int reading; // the current value read from the input pin
int current_state = LOW; // the debounced input value
// the following variable is a long because the time, measured in milliseconds,
// will quickly become a bigger number than can be stored in an int.
long time = 0; // the last time the output pin was sampled
int debounce_count = 10; // number of millisecond/samples to consider before declaring a debounced input
void setup()
{
pinMode(inPin, INPUT);
pinMode(outPin, OUTPUT);
digitalWrite(outPin, current_state); // setup the Output LED for initial state
}

## Slide 41
void loop()
{
// If we have gone on to the next millisecond
if(millis() != time)
{
reading = digitalRead(inPin);
if(reading == current_state && counter > 0)
{
counter--;
}
if(reading != current_state)
{
counter++;
}
// If the Input has shown the same value for long enough let's switch it
if(counter >= debounce_count)
{
counter = 0;
current_state = reading;
digitalWrite(outPin, current_state);
}
time = millis();
}
}
millis () function:
This function is used to return the number of milliseconds at the time, the Arduino board begins running the current program, that is, this Arduino function returns the present time in milliseconds from the moment the Arduino board is powered on or reset. The return value of millis is the number of milliseconds through an unsigned long variable since the program in Arduino started.
This number overflows i.e., goes back to zero after approximately 50 days.
millis() function Syntax. millis(); This function returns milliseconds from the start of the program.

## Slide 42
Standard Values of Resistance (Commercially Available in the Market):

## Slide 43: References
ATMega328 manual
http://www.ganssle.com/debouncing-pt2.htm
https://mansfield-devine.com/speculatrix/ 2018/04/debouncing-fun-with-schmitt-triggers-and-capacitors/

## Slide 44: Thanks for Attending….
?